## Slide 1: Chapter six
Mixing

## Slide 2: OUTLINE
Dynamic Range
Compression, Limiting & Normalization
Expansion
Gating and Ducking
Noise Reduction
Mixing theories
Figure and Ground/ Signal to Noise
Panning
Point of Audition

## Slide 3: Dynamic Range
Which has the MOST and LEAST dynamic range?

## Slide 4: Compression
Reduces dynamic range over whole file
(“squashes”) by Cutting High and boosting Low

## Slide 5: Compression Threshold
How loud signal is before compression is applied

## Slide 6: Compression ratio
Change in output levels above the threshold
4:1 ratio: 3dB reduction above threshold (For every 4dB, reduce to 1dB)

## Slide 7: Examples: Compression Ratio
Raw file
2: 1 ratio
7:1 ratio

## Slide 8: Compression: Attack Time
How quickly amplitude is reduced once input exceeds threshold
threshold
Attack time
Compression begins

## Slide 9: Compression: Release Time
How quickly compressor releases after sound wave drops below threshold
Release time

## Slide 10: Limiting
Compression ratio > 10:1
Raw file
Limiting to -10dB

## Slide 11: Compression Tips
Don’t over-compress. Some dynamic range is good! (keep ratio under 5:1)
Settings in this effect work together. Adjust them together and see how they affect the output.
Takes a lot of practice—listen carefully
It will increase background noise
Some fast attacks can cause low frequencies to distort

## Slide 12: Why compress?
Makes overall average sound louder  advertising on TV
Prevents audience from “riding the remote”
Evens out vocal recordings
“pumping” percussion e.g. drums -> heavily used in dance music

## Slide 13: The Loudness Wars
Zeitgeistmastering.com

## Slide 14: “Loudness war” explanation video
https://www.youtube.com/watch?v=3Gmex_4hreQ

## Slide 15: Normalization
Sets loudest peak of file to that level & adjusts rest to match
Maintains dynamic range, adjusts overall level.
Original file
Normalized to -5 dB

## Slide 16: Expander (*no expander in Audacity)
FabFilter Pro-G expander
Waves
PSE

## Slide 17: Expansion
Opposite of compression: expands dynamic range by reducing sounds below threshold
Threshold: -12 dB

## Slide 18: Gating = Harsh Expander
Gate at -12dB threshold

## Slide 19: Hard gate to -6dB

## Slide 20: Noise Gate in Audacity

## Slide 21: Ducking
Reduces signals above a threshold by range by using second control file to set where ducking takes place
Common use in radio to duck music under voice

## Slide 22: Ducking
File to duck
Control file
Result--ducked
Control file

## Slide 23: Side-Chaining
Using a control file to feed into an effect to alter the effect’s amount
Mostly used on compression-related effects

## Slide 24: Noise Reduction
Control = “Noise profile”
Noise profile: sample of noise you want to eliminate

## Slide 25: Mixing Theories

## Slide 26: 3 dimensions of mixing

## Slide 27: Near vs. Far
Louder
More EQ in mid to high frequency
Less reverb/delay
Hard compression
Unusual effects  stick out

## Slide 28: High and Low
EQ: high frequencies up high, low frequencies down low
Resonators in our body: head = high, gut = low

## Slide 29: Left to right : Panning
Stereo positioning:
Sweet spot is at
corner of equilateral triangle (when using loudspeakers!)
Sweet spot
60º

## Slide 30: Panning in Audacity

## Slide 31: Advanced stereo panning: Waves S1 ($)

## Slide 32: Advanced Stereo Imaging: Ozone Imager

## Slide 33: Phantom Images

## Slide 34: Figure and Ground
Foreground
Midground
Background
Photo: Earl Noble, http://vocm.com/news/rnc-urges-caution-near-emergency-scenes/

## Slide 35: Masking : NOISE
White noise = broad frequency spectrum, evenly across entire frequency
Pink noise = white noise with high frequencies attenuated
Brown noise = exaggerated pink noise (even more attenuation)

## Slide 36: Point of Audition
Where is the audience?
Analogous to POV in film– position as “in” a scene or outside a scene.

## Slide 37: Point of Audition
Emphasis in mix through EQ, panning and volume
Use of filters
Use of effects
Microphone selection
Microphone location
Channel/speaker location
Spatial location of sounds

## Slide 38: Creative versus technical mix
Psychological state of character
Altered physical state of character
Focus audience’s attention